## Slide 1: DER Opportunities in the Pacific Northwest
Ken Nichols
ken@eqlenergy.com 503-438-8223
Notes: EQL Energy – started in 2010 to support customer side smart grid technology/program development and utility planning and operations (capacity)
Clients include utilities and product/service vendors. As such, I think we have a balanced view of the market place and its policies.
We were asked to write a paper for Western Interstate Energy Board on emerging distribution issues in WECC.
I do confess: I PVs on my roof and EV in garage, and recently installed an energy disaggregation meter. Right now, my house has capability to provide voltage support, balancing reserves, load shifting if my utility asked.
We just finished a paper for Western Interstate Energy Board which is the energy policy offshoot for the Western Governors Association.
You can find the paper on our website.
Distribution investment/operation has not received as much attention from regulators/policy makers. Discussions began when utilities were proposing AMI investments/Distribution Management. With increasing DER there are more opportunities are available for customers to procure cost effective energy and utilities to get grid resources.
DER includes: PV, Energy Storage, CHP/backup generators, EV charging/discharging, and load management
CA added Energy Efficiency to the Distribution Resources Planning guidance in order to compare with other choices.
I have an electric car, lease is $117/mo and at current gas/electric prices saving $348/yr in fuel.
I plug my car in all night and I would swap 1) charge to be controlled off in emergencies for 2) lower electric rates
Today distribution planning/investment varies from
Gold plate plenty of room for capacity growth TO
Run the system to the edge, and pay attention to thermal limits
Story: In preparing this paper I spoke with a distribution planner that described their planning process, and it followed the axiom
“if it ain’t broke, don’t fix it” = fully utilized
He shared that during his long career he had only lost a handful of lines to overcapacity or thermal

## Slide 2
NPCC 7th Plan 2021 Demand Response Winter 600-1,000MW
Source: Northwest Power and Conservation Council, Mar. 2015
5,000
4,000
3,000
2,000
1,000
-­‐
Year
6,000
7,000
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
2027
2028
2029
2030
2031
2032
2033
2034
2035
Cumulative
Winter Capacity (MW)
Demand Response Conservation
US 2013 DR > 28,000 MW
Notes: PNW has historically been capacity

## Slide 3
DER Spend in the PNW
2022 WECC (MW)1
Distributed Resource | 2021 Forecast | 5 yr Budget | Sources and Assumptions
 | MW | $MM | 
DR Reliability | 145 | $45 | NPCC, utility IRPs, WIEB study, $100/kW-yr
DR Peak Reduction | 1,000 | $195 | NPCC early target, <4% peak, summer (500) and winter (500), $60/kW-yr
Distributed Solar | 332 | $663 | NPCC distributed, 2014 E3 TEPPC DG reference, $2,000/kW
CHP | 238 | $333 | NPCC, 2014 E3 TEPPC DG reference, $1,400/kW
Storage | 55 | $176 | WA and OR law, PUC, $1,400/kW
CVR (aMW) | 33 | $29 | NPCC aMW estimate by 2021, $0.10/kWh
DSG (non-spin) | 210 | $231 | PGE has 100MW today, $200/kW-yr
DER Total | 2,013 | $1,672 | 
EE Total (aMW) |  | $2,105 | Historical spend 2014 budget $421, times 5 years
Notes: Most in the PNW think that this DER growth will be in the south. NOT the CASE
1. Based on insolation levels, the city of Helena can produce roughly 2,250 kilowatt hours of solar electric power annually from a 1,000 watt utility-connected solar electric system, which is more than Jacksonville, Florida.
2. CHP being evaluated examples: data centers, lumber mills, universities, hospitals, military complexes and colleges.
One of our college campus is evaluating an 8MW CHP system to provide heatboth heating and cooling

## Slide 4
Summary of IOU resource plans
Notes: Tesla/Solar City
Utility business models in transition
Survey of 400 utility execs 40% said growth opportunity is with DER. @ Distributech
Allow ratebase for grid modernization, reliability improvement, and DER
Grid Modernization, Reliability, IT
. FLISR – Fault Location, Isolation, Service Restoration
. DMS –
. Distribution Automation
. OMS
Value of Solar and Net Metering
. Maine approves $.33/kWh Solar value (double rate)
. Idaho Power estimated value at $.04 to $.08/kW
Distribution Resources Planning and Operations
Require it whenever utility is proposing investment to support load growth. (T/D/G)
Do DRP on top 10% of substations requiring upgrade
Engage solar and other DER vendor and trade allies.
Technology (trade allies and vendors) and Customers
We recommend utilities rely on Energy Efficiency and Trade Allies to engage customers
Manage technological obsolescense. Produce roadmaps
Legislative actions that work
  Value of solar DER … is just the beginning
  Rate Strategy (reflect Utility costs, pilot>demo>scale)
  Combined Heat and Power (WA E2SHB 1095)
  Distribution Resources Planning (CA AB327, WA 2045)
  Demand Response follow Energy Efficiency (NPCC 7th Plan)
  Support (Mandate) Standards
Hawaiian Electric in their Distributed Generation Interconnection plan in 2014 estimated $194MM in distribution investments to accommodate 902MW of solar

## Slide 5
Demand Response by Utility
 | 2021 System Load |  |  | Demand Response (MW) |  |  | 
Utility | Midrange Peak Load (MW) | Energy (GWh) | % PNW Capacity | 2015 Existing (summer) | IRPs (summer and winter) | 2021Target (Summer and Winter) | 5 yr Target Budget
 | MW | GWh | % | MW | MW | MW | $MM
Avista | 2,720 | 14,673 | 7% | 0 | 0 | 54 | $11.4
Bonneville Power Administration | 10,463 | 53,972 | 28% | 0 | ? | 209 | $43.9
Chelan Co PUD | 722 | 4,056 | 2% | 0 | 0 | 14 | $3.0
Douglas Co PUD | 424 | 1,975 | 1% | 0 | 0 | 8 | $1.8
Grant Co PUD | 858 | 5,177 | 2% | 0 | 0 | 17 | $3.6
Portland Gen Electric | 4,220 | 23,463 | 11% | ? | ? | 84 | $17.7
Idaho Power | 4,159 | 16,605 | 11% | 378 | 378 | 378 | $79.4
Northwestern (MT) | 1,833 | 11,390 | 5% | 0 | 0 | 37 | $7.7
PacifiCorp PNW | 4266 | 22,914 | 11% | 162 | 162 | 162 | $34.0
Puget Sound Energy | 5,322 | 26,485 | 14% | 0 | 121 | 121 | $25.4
Seattle City Light | 1,909 | 10,751 | 5% | 0 | 0 | 38 | $8.0
Tacoma Power | 1,040 | 5,480 | 3% | 0 | 0 | 21 | $4.4
Pacific Northwest | 37,936 | 196,941 | 100% | 540 | 661 | 1,145 | $240.4
 | Energy Efficiency |  |  |  |  |  | $2,105.0
Notes: Tesla/Solar City
Utility business models in transition
Survey of 400 utility execs 40% said growth opportunity is with DER. @ Distributech
Allow ratebase for grid modernization, reliability improvement, and DER
Grid Modernization, Reliability, IT
. FLISR – Fault Location, Isolation, Service Restoration
. DMS –
. Distribution Automation
. OMS
Value of Solar and Net Metering
. Maine approves $.33/kWh Solar value (double rate)
. Idaho Power estimated value at $.04 to $.08/kW
Distribution Resources Planning and Operations
Require it whenever utility is proposing investment to support load growth. (T/D/G)
Do DRP on top 10% of substations requiring upgrade
Engage solar and other DER vendor and trade allies.
Technology (trade allies and vendors) and Customers
We recommend utilities rely on Energy Efficiency and Trade Allies to engage customers
Manage technological obsolescense. Produce roadmaps
Legislative actions that work
  Value of solar DER … is just the beginning
  Rate Strategy (reflect Utility costs, pilot>demo>scale)
  Combined Heat and Power (WA E2SHB 1095)
  Distribution Resources Planning (CA AB327, WA 2045)
  Demand Response follow Energy Efficiency (NPCC 7th Plan)
  Support (Mandate) Standards
Hawaiian Electric in their Distributed Generation Interconnection plan in 2014 estimated $194MM in distribution investments to accommodate 902MW of solar

## Slide 6
Integrated Demand Side Management
Category | Description | Example
Class 1 | dispatchable or scheduled firm capacity (MW) | Demand Response, Curtailment, storage, DSG, CVR capacity
Class 2 | non-dispatchable, firm energy (MWh) and capacity (MW) | Energy and Capacity Efficiency, permanent load shift, CHP, Solar, CVR energy
Class 3 | price responsive energy (MWh) and capacity (MW) | TOU, CPP, PTR: enabled with technology and double savings
Class 4 | Non-incented energy and capacity through broad market transformation, customer education and communication | NEEA, Strategic Energy Management, HEM, smart thermostats and information
Integrated DSM
Combine elements and values during planning and procurement
Combine Marketing and Customer perspective
Distribution Resource Planning
  Details - season, time of day, duration per day, hours per year, MW amount, response time (day ahead, 10 minutes)
  Capacity type - system capacity, contingency reserves (20 minute), balancing reserves (Inc/Dec)
  Location and Value – When considering load growth and T&D cost/constraints, DSM and DER will have different locational values and opportunities.
Notes: Demand Response is DSM focused on capacity. From customer perspective Energy and Capacity DSM will be marketed by EE institution. Integrated DSM.
Utilities will develop community projects and build infrastructure to support capacity DSM (e.g., distribution automation, communication of critical peak periods, or calling reserves. Capacity DSM will be dispatcahble.
Utilities becoming more comfortable with distributed storage and generation
All of these will be on the distirbuiton system

## Slide 7
1300MW Distributed Solar 2021
NPCC 7th Plan forecast

## Slide 8
Regulatory Effort
  Oregon - SB1547, SB1574, SB2193. State incentives for solar, storage, CHP
  OPUC UM1708 (PGE DR pilots), UM1716 (value of solar), UM1751 (storage), Implementation of SB1547, DR cost effectiveness
  WA – SB2346, SB6166. State incentives for solar, storage, CHP. Distribution System Collaborative
  WUTC – IRP rulemaking, PSE DR RFP (June 15, 2016), net metering, IOU IRPs, WA DISCo
  Montana/Idaho – Utility IRPs avoid DERs and target NEM repeal

## Slide 9
Oregon SB 1547

## Slide 10: Questions and Discussion